## Slide 1
Project ID | CE_AIML_31
Enrollment No | 2301030600043, 2301030600045, 2301030600049
Name | Prem Deshani, Kavya Kothari, Mehulsinh Rathod
Branch | BTech. CE-AIML
Guide Name | Ms Vishwa Patel
Minor Project
1010063491
A.L.E.R.T.

## Slide 2: Index
Introduction
Background and Motivation
Relevance and Importance
Literature review
Research Gap
Objectives
Required Dataset, Tools and Technology
Methodology
Result
Conclusion
Future Work
References

## Slide 3: Introduction
Automotive Safety Crisis: Driver fatigue causes over 20% of commercial vehicle crashes worldwide, making real-time Driver Monitoring Systems (DMS) essential.
Facial Behavioral Analysis: Uses non-invasive computer vision to analyze eye openness (EAR), yawning (MAR), PERCLOS, and head pose angles.
The Non-IoT Edge Approach: Executes 100% on-device AI inference directly on embedded hardware (Raspberry Pi 5 / NVIDIA Jetson Orin Nano).
Key Technical Advantages: Delivers sub-5ms latency, complete offline reliability, zero cellular bandwidth cost ($0/mo), and total data privacy (GDPR compliance).
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 4: Background and Motivation
Flaws of Cloud/IoT Architectures: Cloud-dependent systems suffer from network latency jitter (150ms–500ms+), rendering micro-sleep alerts ineffective.
Connectivity Dead Zones: Vehicles frequently navigate tunnels, mountain passes, and rural highways where 4G/5G cellular signal is lost.
Biometric Privacy Liabilities: Transmitting high-definition facial video streams to cloud servers poses severe GDPR and biometric privacy risks.
High Operating Expense: Cloud video streaming costs $15–$30/month per vehicle in cellular data and cloud server compute fees.
Edge Motivation: An autonomous, sub-5ms on-device system guarantees 100% alert reliability anywhere without recurring costs.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 5: Relevance and Importance
Sub-5ms Compression Pipeline: Combines MediaPipe BlazeFace + Face Mesh backbones with Quantization-Aware Training (QAT INT8) for sub-5ms inference.
24/7 NIR Lighting Robustness: Implements 850nm / 940nm Near-Infrared illumination with adaptive CLAHE contrast enhancement for day & night operation.
Eyewear & Sunglasses Robustness: Features dual-wavelength NIR penetration and dynamic fallback to Mouth Aspect Ratio (MAR) + Head Nodding when eyes are occluded.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 6
Relevance and Importance
6
Personalized Calibration (<10s): Automatically calculates baseline thresholds (EAR_thresh = mean - 2.5*std) without manual configuration.
Commercial Relevance: Reduces fleet accident rates, lowers insurance liabilities, and scales easily across commercial trucking, buses, and ride-shares.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 7: Literature Review
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY
Sr.No | Ref.No (Citation) | Algorithm Used | Dataset | Result | Findings
1 | R1 - Soukupova & Cech (2016) | EAR + SVM classifier | Not specified in source | Real-time blink detection demonstrated | EAR scalar characterizes eye openness from 6 landmarks per eye
2 | R3 - Kazemi & Sullivan (2014) | Ensemble of Regression Trees (ERT) | Not specified in source | ~1ms face alignment speed | Basis for dlib's 68-point shape predictor
3 | R4 - Lugaresi et al. (2019) | MediaPipe Face Mesh | Not specified in source | Real-time mobile/edge inference | 468-point landmark tracking optimized for edge devices
4 | R5 - Multi-Feature Study (2023) | EAR + MAR + PERCLOS fusion | Not specified in source | Not specified in source | Adaptive-threshold multi-signal fatigue detection
5 | R7 - Survey (2024) | CNN / ViT + geometric feature fusion | Multiple (survey) | Not specified in source | Hybrid geometric + deep learning improves robustness
6 | R8 - Guo et al. (2020) | Zero-DCE (Zero-Reference Deep Curve Estimation) | Low-light image benchmarks | Not specified in source | Low-light enhancement without paired training data
7 | R9 - Pizer et al. (1987) | CLAHE (Contrast Limited Adaptive Histogram Equalization) | N/A | N/A | Localized histogram equalization limits noise amplification
8 | R10 - Multi-Spectral Study (2022) | Multi-spectral CNN | Thermal + visible imagery | Higher accuracy across all lighting conditions | Multi-spectral fusion outperforms single-spectrum detection
9 | R11 - NTHU-DDD Benchmark | Transformer-based model / Hybrid VGG16+LeNet | NTHU-DDD | 99.71% accuracy / 98.69% accuracy | Multi-condition dataset (day/night, glasses/sunglasses occlusion)
10 | R12 - UTA-RLDD Benchmark | YOLOv5/v8 / KNN | UTA-RLDD | 100% precision/recall (mAP@0.5: 99.5%) / 98.89% accuracy | 60 subjects, naturalistic webcam recordings, 3 alertness states

## Slide 8: Research Gap
Single-Metric Blind Spot: Most cited work (Soukupová EAR, Garces MAR) validates one signal in isolation, without fusing eye, mouth, and head-pose channels into one real-time classifier.
No Edge-Optimized Multi-Metric Pipeline: PERCLOS and CNN-based approaches are validated on desktop/GPU hardware; none combine INT8-quantized, sub-5ms inference with a 9D multi-signal feature vector on sub-$100 hardware.
Limited NIR / Occlusion Robustness: Reviewed literature (Dzyakanchuk, Acharjee) targets visible-light daytime conditions; night driving and sunglasses occlusion are largely unaddressed together.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 9: Research Gap
No Personalized Calibration in Embedded Studies: Existing embedded DMS work uses fixed EAR/MAR thresholds, ignoring individual eye-shape variation (e.g., monolids) that causes false alarms.
Gap ALERT Addresses: A per-driver-calibrated, multi-metric (eye + mouth + head-pose), edge-deployable pipeline validated across lighting and eyewear conditions not demonstrated as one system in current literature.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 10: Objectives
To prevent fatal road accidents and save lives by detecting driver fatigue and micro-sleeps in real time before loss of vehicle control occurs.
To develop a completely non-intrusive safety system that monitors driver alertness using standard camera vision without requiring wearable sensors or manual driver setup.
To ensure 100 percent offline and privacy-preserving operation, enabling reliable fatigue monitoring on highways and tunnels without relying on cellular networks or cloud infrastructure.
To build an affordable, edge-deployable solution that can be easily integrated into commercial trucking fleets, public transport, and consumer vehicles.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 11: Required Dataset, Tools and Technology
Technology | Purpose | Version / Spec
Raspberry Pi 5 | Edge compute hardware platform | -
NVIDIA Jetson Orin Nano | High-end edge compute platform | -
Google Coral USB Edge TPU | Edge inference accelerator | $60
Hailo-8L HAT | Edge inference accelerator | 13 TOPS
NIR LED arrays | Night-driving illumination | 850nm / 940nm
Bandpass optical filters | Optical hardware for NIR imaging | Narrow bandpass
No-IR-Cut camera sensor | Optical hardware for NIR imaging | -
Table 1 — Hardware & Optical
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 12: Required Dataset, Tools and Technology
Technology | Purpose | Version / Spec
OpenCV | Camera I/O, solvePnP, ROI crop, HUD | 4.8+
MediaPipe FaceLandmarker | 3D facial landmark extraction | 468 landmarks, 6.7MB TFLite
XNNPACK CPU delegate | Landmark inference backend | ~8-15ms, LIVE_STREAM @ 640x480
LightGBM | Gradient boosted trees (Model A) | 4.0+
scikit-learn | Preprocessing + RF POC baseline | -
PyTorch | GRU (Model B) + CNN eye-patch (Model C) | 2.1+
ONNX Runtime | Cross-platform edge serving | 1.16+
NumPy / SciPy | Feature engineering, EMA drift | -
imbalanced-learn | SMOTE for L3 class imbalance | -
Pandas | Dataset loading, label alignment | -
Table 2 — ML / CV Libraries
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 13: Required Dataset, Tools and Technology
Technology | Purpose | Version / Spec
Python | Core runtime | 3.10+ / 3.11 (dev)
C++ | High-performance frame ingestion/inference | C++17
Git / VS Code | Dev environment | -
OpenVINO | Edge deployment target | Intel NPU
TensorRT | Edge deployment target | INT8 (Jetson)
Table 3 — Runtime, Dev & Deployment
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 14: Required Dataset, Tools and Technology
Dataset | Subjects | Size | Labels | Role
UTA-RLDD | 60 | ~6.4M frames, 95 GB | Alert / Low Vigilance / Drowsy (→ L0-L2) | Primary training set
NTHU-DDD | 36 | ~14 GB | Drowsy / Non-Drowsy (frame-level) | Glasses occlusion + low-light robustness
YawDD | 107 | ~8 GB | Normal / Talking / Yawning | Real dashcam perspective
MRL Eye | 37 | 84,898 images, ~2 GB | Open / Closed (per image) | Trains Model C (CNN eye-patch) only
Table 4 — Training datasets
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 15: Methodology
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 16: Result
POC Classifier Performance: The Random Forest baseline (30 trees) achieves 100% precision/recall on the synthetic 9D benchmark feature matrix — confirming the feature engineering (EAR, PERCLOS, MAR, MOE, head pitch) cleanly separates the four fatigue classes.
Real-Time Pipeline Validated: Live webcam HUD (orchestrator.py) successfully runs MediaPipe landmark extraction, 10-second calibration, and live L0–L3 classification with on-screen probability breakdown.
Inference Speed: Classifier inference measured at sub-3ms per frame, consistent with edge-latency targets.
Caveat to state honestly: These results are on synthetic/POC data, not yet the real-world benchmark datasets (UTA-RLDD, NTHU-DDD, YawDD, MRL Eye) — real-dataset evaluation is pending (see Future Work).
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 17: Conclusion
ALERT demonstrates that a fully offline, edge-deployable driver fatigue detection pipeline is technically feasible using MediaPipe landmarks and a compact multi-signal feature vector.
The POC validates the core hypothesis: geometric + temporal features (EAR, PERCLOS, MAR, head pose) are sufficient for a classical ML model to separate fatigue severity levels with high accuracy on controlled data.
The architecture is designed from the outset for sub-5ms, sub-$100 edge hardware, directly addressing the connectivity, latency, and privacy gaps of cloud-based DMS alternatives.
Current stage is Proof-of-Concept only; production-grade accuracy claims require training and validation on real driver datasets, which is the immediate next step.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 18: Future Work
Real-Dataset Training: Train and validate on UTA-RLDD, NTHU-DDD, YawDD, and MRL Eye datasets to replace/augment the synthetic POC data.
Ensemble Model Completion: Implement and fuse the full 3-model architecture (LightGBM + GRU sequence model + CNN eye-patch classifier) described in the technical design, beyond the current single Random Forest.
NIR Hardware Integration: Add 850/940nm near-infrared illumination and camera support for night-driving and eyewear-occlusion robustness.
Edge Deployment & Quantization: Port the pipeline to Raspberry Pi 5 / Jetson Orin Nano with INT8 quantization (TensorRT/OpenVINO) to hit the sub-5ms target on real hardware.
Fleet & Vehicle Integration: Add CAN bus / buzzer / seat-vibration output hooks for real vehicle deployment and pilot testing.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 19: References
[1] Soukupova, T., & Cech, J. (2016). Real-Time Eye Blink Detection Using Facial Landmarks. Computer Vision Winter Workshop.
[2] Dinges, D. F., & Grace, R. (1998). PERCLOS: A Valid Psychophysiological Measure of Alertness. US Dept of Transportation.
[3] Dzyakanchuk, A., et al. (2022). Low-Power Face Detection on Raspberry Pi for Automotive DMS. IEEE Access.
[4] Acharjee, S., et al. (2020). Edge-Based Driver Drowsiness Monitoring on Embedded Hardware. SN Computer Science.
[5] Garces, M., et al. (2021). Automated Yawn Detection Using Mouth Aspect Ratio. IEEE Sensors Journal.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 20: References
[6] MediaPipe Face Mesh Topology (468 3D Landmarks). Google AI Edge Documentation (2023).
[7] NVIDIA TensorRT INT8 Developer Guide for Jetson Orin Platform (2024).
[8] Hailo-8L Dataflow Compiler & Software Suite User Guide (2024).
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY