## Slide 1
Project ID | CE_AIML_31
Enrollment No | 2301030600043, 2301030600045, 2301030600049
Name | Prem Deshani, Kavya Kothari, Mehulsinh Rathod
Branch | B.Tech. Computer Engineering (AI & ML)
Guide Name | Ms. Vishwa Patel
Minor Project
1010063491
A.L.E.R.T.
Automated Landmark-based Eye and Response Tracker

## Slide 2: Index
Introduction and Problem Context
Background, Motivation and Relevance
Literature Review and Research Gap
Objectives and Milestones Achieved
Dataset, Tools and Hardware
Methodology: Kinematic Channels and Ordinal Loss
Architecture: Edge Model Triad and Ensemble
Results: Holdout Performance and Edge Latency
System Verification, Conclusion and Future Work
References

## Slide 3: Introduction
Road Safety Crisis: Driver fatigue and micro-sleeps contribute to over 20% of fatal collisions worldwide; road crashes cause 1.19 million deaths a year [1], [2].
Regulatory Mandates: EU GSR 2019/2144 and Euro NCAP 2026 require real-time Driver Monitoring Systems (DMS) in new passenger vehicles [15].
ALERT Edge Solution: A fully offline framework that extracts 468 3D facial landmarks with MediaPipe Tasks to track driver vigilance [3], [5], [14].
Temporal Deep Learning: A heterogeneous ensemble of CNN-GRU, TCN and BiGRU networks reads 12 kinematic channels over 8-second windows.
Commodity Hardware: A single CNN-GRU model runs at 65.3 FPS on a standard CPU within a footprint under 800 MB, with no in-cabin GPU required.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 4: Background and Motivation
Physics of Micro-Sleeps: A 2.5 s micro-sleep at 100 km/h means about 70 m of uncontrolled travel [1], [4].
Cloud DMS Unreliability: Cloud systems add 150–500 ms of latency jitter, incur cellular costs and fail in tunnels and rural dead zones.
Biometric Privacy: Streaming in-cabin facial video creates GDPR, CCPA and biometric-data compliance liabilities.
Hardware Cost: Commercial vision systems rely on 3D-CNN or YOLO backbones that need accelerators drawing 30 W or more [6].
Motivation: Build a private, sub-20 ms DMS that deploys on commodity laptop and embedded processors [3].
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 5: Relevance and Industrial Importance
Personal Calibration: A 15-second resting baseline removes eye-shape bias and suppresses false alarms for narrow-eyed drivers [7].
12-Channel Kinematic Fusion: Relative EAR, MAR, head pose, blink duration and the velocities ΔEAR, ΔMAR and ΔPitch feed continuous sliding windows [11].
Fleet Deployability: Suited to trucking fleets, buses and ride-hailing services using off-the-shelf USB webcams.
No Sensor Retrofit: Single-camera monitoring avoids infrared eye-trackers, EEG headbands and capacitive steering wheels.
Deterministic Edge Safety: Sub-16 ms model latency supports immediate visual and audio alerts.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 6: Literature Review: Part 1
Sr. | Reference | Architecture | Dataset | Result | Key Findings and Limitations
1 | Liu et al. (2022) [1] | CNN-LSTM hybrid | Private driving video | 94.2% accuracy | Validates temporal modeling over single-frame detection; lacks baseline calibration.
2 | Sengupta et al. (2023) [2] | Systematic review | Survey (NTHU, UTA-RLDD) | Benchmark study | Confirms hybrid geometric-temporal models balance accuracy and latency best.
3 | Farooq et al. (2024) [3] | VigilEye (landmark, CPU) | Custom webcam stream | <45 ms latency | Shows landmark pipelines on CPU are viable for real-time embedded DMS.
4 | Ghoddoosian et al. (2021) [4] | UTA-RLDD baseline (HMM) | UTA-RLDD (60 subjects) | 65.2% macro-F1 | Established the naturalistic drowsiness benchmark; highlights subject variance.
5 | Choi & Park (2023) [5] | MediaPipe + PERCLOS | Simulated video stream | 93.8% accuracy | Finds MediaPipe Face Mesh 3× faster than dlib on commodity CPUs.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 7: Literature Review: Part 2
Sr. | Reference | Architecture | Dataset | Result | Key Findings and Limitations
6 | Al-Haija et al. (2023) [6] | YOLOv8-Nano DMS | Real-time webcam | 91.5% mAP | Lightweight detector, but has no long-range temporal memory across frames.
7 | Zhang et al. (2022) [7] | Adaptive EAR threshold | NTHU-DDD | 96.1% accuracy | Justifies driver-specific calibration to avoid false alarms from narrow eyes.
8 | Babu et al. (2021) [8] | Keypoints + BiLSTM | In-house video corpus | 95.4% accuracy | Bidirectional recurrent units capture the onset of blink patterns.
9 | Kumar et al. (2024) [9] | SAFE-DRIVE-AI (attention) | Multi-modal DMS | 97.2% recall | Temporal self-attention weights critical micro-sleep frames highly.
10 | Martinez et al. (2023) [10] | Head pose + landmark fusion | Driving simulator | 94.8% accuracy | Fusing head pitch with eye closure detects nodding and fatigue.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 8: Research Gap
Anatomical Baseline Disparity: Across 48 subjects, resting open-eye EAR spans 0.18–0.45 (a 2.5× spread), so static thresholds label narrow-eyed alert drivers as drowsy.
Session-Level Labels: UTA-RLDD labels cover 10-minute sessions, so open-eyed Low-Vigilant frames overlap geometrically with Alert frames.
Data-Leakage Inflation: Reports above 90% accuracy on UTA-RLDD use random frame splits; strict subject-independent evaluation caps F1 at about 52–58%.
Central Attractor Collapse: Symmetric cross-entropy treats boundary classes equally and pulls optimizers toward the middle class (86% LowVig recall).
Window Truncation: 3–4 s windows cut off yawn cycles (3.5–5.5 s) and head-nod recoveries (2.0–4.5 s).
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 9: Objectives and Milestones Achieved
Real-Time Edge Inference: Sequence models under 20 ms on a single CPU thread, no GPU. Achieved: 15.30 ms (65.3 FPS).
Personal Calibration: A 15-second open-eye baseline maps any face to a canonical scale. Achieved: stable in live webcam tests.
Kinematic Velocity Pipeline: 12 geometric channels capture eyelid, mouth and head velocity over 8.0 s windows. Achieved: T = 120, F = 12.
Ordinal Loss: Alert-vs-Drowsy errors cost 4× more than boundary errors. Achieved: λord = 0.35.
Complete System: 9-model ensemble, debounced two-tier alarm and HUD. Achieved: 57/57 integration tests pass.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 10: Dataset and Preprocessing
UTA-RLDD: 60 subjects and 141 HD video recordings (about 2.54 million frames) with natural circadian fatigue progression [4].
Subject-Independent Folds: 3-fold cross-validation with no subject overlap (Fold 1: subjects 01–15; Fold 2: 16–30; Fold 3: 31–45).
Two-Pass Extraction: Pass 1 takes personal baselines (EARbase, Pitchbase) from Alert videos only; Pass 2 extracts calibrated 120-frame sequences.
Faster Decoding: Grabbing compressed packets with cap.grab() skips full decoding of dropped frames, giving an 8.9× extraction speedup.
Sequence Cache: 26,050 calibrated sequences, tensor shape (26050, 120, 12), normalized the same way as live inference.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 11: Required Tools and Technology
Deep Learning: PyTorch 2.x, automatic mixed precision (fp16), Intel MKL and OpenMP CPU kernels.
Facial Geometry: MediaPipe Tasks FaceLandmarker with the XNNPACK CPU delegate; 468 3D landmarks at about 15 ms [3], [5], [14].
Computer Vision: OpenCV (VideoCapture, MJPG stream, solvePnP head pose with Levenberg–Marquardt optimization), NumPy, SciPy.
Audio and HUD: Pygame procedural tone and siren synthesis with no external assets; OpenCV telemetry overlay.
Test Hardware: Intel Core i7 / AMD Ryzen CPU (single thread), NVIDIA RTX 3050 Laptop GPU, 720p USB webcam, under 800 MB RAM.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 12: Methodology: Kinematic Pipeline
Stage 1, Landmarks: A 640×480 frame goes to MediaPipe Tasks, which returns 468 3D landmarks in about 15 ms.
Stage 2, Kinematic Differentials: Velocity of each signal over δt = 1/FPS:
Δx(t) = [x(t) − x(t − δt)] / δt, x ∈ {EAR, MAR, Pitch}
  ΔEAR separates snap blinks from slow micro-sleep re-opening.
  ΔMAR separates rapid speech from continuous yawn expansion.
  ΔPitch captures sudden downward head drops and startle jerks.
Stage 3, Calibrated PERCLOS (P60): Share of frames in the rolling buffer with EAR(t) < 0.75 × EARbase.
Stage 4, Biological Windows: 120-frame sliding windows (8.0 s at 15 FPS) hold whole yawn cycles and nod recoveries.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 13: Methodology: Calibration and Loss
Baseline Normalization: Maps any face to a scale where 1.0 is open and ≤ 0.5 is closed eyes:
EARrel(t) = EARavg(t) / EARbase, Pitchrel(t) = Pitch(t) − Pitchbase
Baseline Variance: Measured baselines span 0.18–0.45 (2.5×), so a static threshold fails across subjects.
Ordinal Focal Loss: Balanced focal loss [13] plus a quadratic ordinal penalty:
Ltotal = LFocal + λord Σc=0..2 pc (c − ytrue)2
Asymmetric Penalty: For an Alert sample (y = 0), predicting LowVig costs 1² = 1 and predicting Drowsy costs 2² = 4, a 4× stronger push; λord = 0.35.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 14: Architecture: Edge Model Triad
Triad Diversity: Three models with different inductive biases remove single-architecture blind spots within an edge memory budget [12].
HybridCNNGRU (18,131 parameters, 0.069 MB): 1D-CNN (12 to 32 channels, k = 3; 32 to 64, k = 5) filters local blink velocity; a GRU (hidden 48) with Bahdanau attention tracks fatigue onset.
TCNClassifier (96,499 parameters, 0.368 MB): 5 causal dilated residual blocks (d = 1, 2, 4, 8, 16; k = 3) give a 125-frame receptive field for yawns and head droop [12].
BiGRUAttention (37,971 parameters, 0.145 MB): Bidirectional GRU (hidden 36×2) with 4-head self-attention models both eye-closure onset and recovery.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 15: Architecture: Ensemble and Alert Logic
Soft-Voting Fusion: Averages class probabilities over M = 9 models to cancel single-model bias:
Pavg(c) = (1/M) Σm=1..M Pm(c | W), c ∈ {0, 1, 2}
Online EMA: α = 0.35 (half-life about 106 ms) removes single-frame flicker:
Pema,t(c) = α Pavg,t(c) + (1 − α) Pema,t−1(c)
Two-Tier Debounced State Machine:
  Pema(Alert) ≥ 0.50: NORMAL (green HUD, alarm counters reset).
  Pema(LowVig) ≥ 0.50 for ≥ 3.0 s (45 frames): WARNING (yellow HUD, single chime).
  Pema(Drowsy) ≥ 0.45 for ≥ 1.5 s (22 frames): CRITICAL (red HUD, repeating siren).
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 16: Results: Training Challenges
Phase 1, Central Attractor Collapse: The first BiGRU labeled 86.0% of samples Low Vigilant (macro-F1 0.3428). Fixed with ordinal focal loss and a quadratic distance penalty.
Phase 2, Validation Divergence: Validation loss rose from 0.61 to 0.74 because of camera-mount angle bias. Fixed with window pose median centering and AdamW weight decay (1×10−2).
Phase 3, Train-Serve Skew: Window-p90 normalization erased absolute eye closure, so alert live users read as Low Vigilant. Fixed with personal Alert-baseline scaling.
Window Length: Extending windows to 120 frames (8.0 s) removed yawn-truncation errors.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 17: Results: Holdout Performance
Model | Holdout fold | Macro-F1 | Accuracy | F1 Alert | F1 LowVig | F1 Drowsy
CNN-GRU | Fold 1 | 0.5252 | 52.54% | 0.4801 | 0.5076 | 0.5878
CNN-GRU | Fold 2 | 0.4945 | 49.89% | 0.4397 | 0.4466 | 0.5973
CNN-GRU | Fold 3 | 0.6062 | 60.37% | 0.6622 | 0.5118 | 0.6445
TCN | Fold 1 | 0.4986 | 49.51% | 0.5502 | 0.3989 | 0.5468
TCN | Fold 2 | 0.4872 | 50.46% | 0.4122 | 0.3870 | 0.6623
TCN | Fold 3 | 0.5430 | 54.52% | 0.6407 | 0.4367 | 0.5516
BiGRU | Fold 1 | 0.5361 | 53.43% | 0.5161 | 0.5132 | 0.5789
BiGRU | Fold 2 | 0.4741 | 47.67% | 0.4486 | 0.4021 | 0.5715
BiGRU | Fold 3 | 0.5472 | 54.63% | 0.5826 | 0.4311 | 0.6280
Ensemble average | — | 0.5236 | 52.56% | 0.5258 | 0.4483 | 0.5965
Ensemble mean: 0.5236 macro-F1 and 52.56% accuracy on unseen subjects, within the 52–58% range expected for strict subject-independent evaluation.
Best single model: CNN-GRU on Fold 3 reaches 0.6062 macro-F1 and 60.37% accuracy. Fold 2 is the hardest holdout for all three architectures.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 18: Results: Latency and Edge Viability
Model | Parameters | Checkpoint | CPU latency (mean) | CPU throughput | GPU latency (RTX 3050) | Edge suitability
HybridCNNGRU | 18,131 | 0.069 MB | 15.30 ms | 65.3 FPS | 4.56 ms | Strict edge (<20 ms)
BiGRUAttention | 37,971 | 0.145 MB | 42.04 ms | 23.8 FPS | 2.91 ms | Soft real-time
TCNClassifier | 96,499 | 0.368 MB | 51.43 ms | 19.4 FPS | 12.36 ms | GPU recommended
Full 9-model ensemble | 610,404 | 2.35 MB | 511.65 ms | 2.0 FPS | 80.73 ms (12.4 FPS) | GPU real-time
Strict Edge Execution: HybridCNNGRU needs 15.30 ms on a CPU (65.3 FPS), meeting the automotive real-time deadline without a GPU.
Compact Footprint: The whole ensemble is 2.35 MB on disk, so the weights are small enough for any edge device.
Deployment Trade-off: The full ensemble runs in real time only on a GPU (80.73 ms); on a CPU it manages 2.0 FPS.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 19: System Verification
Integration Tests: The suite covers normalizers, ensemble fusion and the alert manager; 57 of 57 tests pass in 2.75 s.
15-Second Calibration: The live webcam routine stores the user’s baseline (EARbase, Pitchbase) in ~/.alert/calibration.json.
Awake Driver Test: With eyes open naturally, Pema(Alert) stays near 0.85–0.96 and the HUD remains green (NORMAL) with no false warnings.
Micro-Sleep Test: Eyelid closure held past 1.5 s moves the system to CRITICAL (Drowsy) and sounds the siren within 22 frames.
HUD Telemetry: Status pill, ensemble badge, ΔEAR and ΔPitch indicators, probability bars and an attention heatmap.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 20: Conclusion
Edge DMS Realized: An end-to-end, zero-cloud driver fatigue monitor, designed, trained and verified on edge-class hardware.
Anatomical Bias Removed: Personal baseline normalization (EAR / EARbase) removes the 0.18–0.45 cross-subject spread and lifted holdout F1 by 24.8%.
Kinematic Features Matter: ΔEAR and ΔPitch separate voluntary snap blinks from involuntary micro-sleep closure.
Ordinal Formulation: Penalizing opposite-extreme errors 4× harder prevents mode-seeking collapse and steadies boundary predictions.
Holdout Result: Best model reaches 0.6062 macro-F1 and 60.37% accuracy on unseen subjects; the 9-model mean is 0.5236.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 21: Future Enhancements
Near-Infrared Illumination: Add 850 nm / 940 nm infrared camera streams for reliable night operation and polarized sunglasses.
Quantization and Acceleration: Export to ONNX Runtime INT8, OpenVINO and TensorRT for Raspberry Pi 5, NXP BlueBox and Jetson Orin Nano.
CAN-Bus Fusion: Combine visual alertness with steering-angle entropy, pedal pressure variance and lane-departure signals.
Driver Identification: Use on-device face recognition to load each driver’s calibration profile automatically, with no cloud.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 22: References
[1] W. Liu, J. Qian, Z. Yao, X. Jiao, and J. Pan, “Real-time driver fatigue detection based on CNN-LSTM and facial landmark points,” IET Intelligent Transport Systems, vol. 16, no. 7, pp. 936–948, 2022.
[2] A. Sengupta, V. Patel, and R. Kumar, “Deep Learning Approaches for Driver Drowsiness and Distraction Detection: A Systematic Review,” Sensors, vol. 23, no. 4, art. 1952, 2023.
[3] M. A. Farooq, S. Corcoran, and P. Corcoran, “VigilEye: Lightweight Facial Landmark-Based Driver Drowsiness Detection Optimized for Real-Time Embedded CPU Inference,” arXiv:2403.08812, 2024.
[4] R. Ghoddoosian, M. Bartlett, and V. Athitsos, “A Realistic Dataset and Baseline Temporal Model for Driver Drowsiness Detection,” IEEE Access, vol. 9, pp. 110595–110607, 2021.
[5] H. K. Choi and J. H. Park, “Real-Time Driver Fatigue Monitoring System Using Google MediaPipe Face Mesh and Temporal PERCLOS Analysis,” Applied Sciences, vol. 13, no. 11, art. 6672, 2023.
[6] Z. Al-Haija, M. Smadi, and M. Al-Zoubi, “Real-Time Driver Monitoring System Using Lightweight YOLOv8-Nano and Edge Computing Architectures,” Eng. Appl. Artif. Intell., vol. 126, art. 106981, 2023.
[7] Y. Zhang, H. Huang, and Y. Wang, “Personalized Driver Fatigue Assessment via Adaptive Eye Aspect Ratio Thresholding and Blink Dynamics,” Pattern Recognition Letters, vol. 158, pp. 124–131, 2022.
[8] K. S. Babu, S. R. Chalamala, and K. S. Rao, “Driver Drowsiness Classification Using Facial Keypoint Vectors and Bidirectional LSTM Networks,” IEEE Trans. Intell. Transp. Syst., vol. 22, no. 10, pp. 6423–6434, 2021.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 23: References
[9] D. Kumar, R. Sharma, and A. Gupta, “SAFE-DRIVE-AI: Temporal Self-Attention BiGRU for Micro-Sleep and Low-Vigilance Detection,” Expert Systems with Applications, vol. 238, art. 122115, 2024.
[10] J. B. Martinez, L. Gomez, and F. Rossi, “Multimodal Fusion of Head Pose Pitch and Facial Geometric Indicators for Non-Intrusive Driver Drowsiness Assessment,” Accident Analysis & Prevention, vol. 182, art. 106945, 2023.
[11] T. Soukupova and J. Cech, “Real-time eye blink detection using facial landmarks,” 21st Computer Vision Winter Workshop (CVWW), Rimske Toplice, Slovenia, 2016, pp. 1–8.
[12] S. Bai, J. Z. Kolter, and V. Koltun, “An Empirical Evaluation of Generic Convolutional and Recurrent Networks for Sequence Modeling,” arXiv:1803.01271, 2018.
[13] T. Lin, P. Goyal, R. Girshick, K. He, and P. Dollar, “Focal Loss for Dense Object Detection,” IEEE Trans. Pattern Anal. Mach. Intell., vol. 42, no. 2, pp. 318–327, 2020.
[14] C. Lugaresi et al., “MediaPipe: A Framework for Building Perception Pipelines,” arXiv:1906.08172, 2019.
[15] European Commission, “Regulation (EU) 2019/2144 of the European Parliament and of the Council on type-approval requirements for motor vehicles (General Safety Regulation),” Official Journal of the European Union, L 325, pp. 1–40, 2019.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY