## Slide 1
Project ID | CE_AIML_31
Enrollment No | 2301030600043, 2301030600045, 2301030600049
Name | Prem Deshani, Kavya Kothari, Mehulsinh Rathod
Branch | BTech. CE-AIML
Guide Name | Ms Vishwa Patel
Minor Project
1010063491
A.L.E.R.T.

## Slide 2: Index
Introduction
Background and Motivation
Relevance and Importance
Literature review
Objectives
Required Tools and Technology
Method/ Approach
Bibliography

## Slide 3: Introduction
Automotive Safety Crisis: Driver fatigue causes over 20% of commercial vehicle crashes worldwide, making real-time Driver Monitoring Systems (DMS) essential.
Facial Behavioral Analysis: Uses non-invasive computer vision to analyze eye openness (EAR), yawning (MAR), PERCLOS, and head pose angles.
The Non-IoT Edge Approach: Executes 100% on-device AI inference directly on embedded hardware (Raspberry Pi 5 / NVIDIA Jetson Orin Nano).
Key Technical Advantages: Delivers sub-5ms latency, complete offline reliability, zero cellular bandwidth cost ($0/mo), and total data privacy (GDPR compliance).
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 4: Background and Motivation
Flaws of Cloud/IoT Architectures: Cloud-dependent systems suffer from network latency jitter (150ms–500ms+), rendering micro-sleep alerts ineffective.
Connectivity Dead Zones: Vehicles frequently navigate tunnels, mountain passes, and rural highways where 4G/5G cellular signal is lost.
Biometric Privacy Liabilities: Transmitting high-definition facial video streams to cloud servers poses severe GDPR and biometric privacy risks.
High Operating Expense: Cloud video streaming costs $15–$30/month per vehicle in cellular data and cloud server compute fees.
Edge Motivation: An autonomous, sub-5ms on-device system guarantees 100% alert reliability anywhere without recurring costs.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 5: Relevance and Importance
Sub-5ms Compression Pipeline: Combines MediaPipe BlazeFace + Face Mesh backbones with Quantization-Aware Training (QAT INT8) for sub-5ms inference.
24/7 NIR Lighting Robustness: Implements 850nm / 940nm Near-Infrared illumination with adaptive CLAHE contrast enhancement for day & night operation.
Eyewear & Sunglasses Robustness: Features dual-wavelength NIR penetration and dynamic fallback to Mouth Aspect Ratio (MAR) + Head Nodding when eyes are occluded.
Personalized Calibration (<10s): Automatically calculates baseline thresholds (EAR_thresh = mean - 2.5*std) without manual configuration.
Commercial Relevance: Reduces fleet accident rates, lowers insurance liabilities, and scales easily across commercial trucking, buses, and ride-shares.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 6: Literature Review
Soukupova & Cech (2016) [R1]: Introduced Eye Aspect Ratio (EAR) using 68 facial landmarks for real-time blink and eye closure detection.
Dinges & Grace (1998) [R2]: Established PERCLOS (Percentage of Eye Closure >= 80% over time window) as the gold standard fatigue metric.
Garces et al. (2021) [R5]: Formulated Mouth Aspect Ratio (MAR) to quantify yawning magnitude and duration.
Dzyakanchuk et al. (2022) [R3]: Evaluated low-power CNN face detection on Raspberry Pi embedded hardware.
Research Gap Addressed: Existing literature lacks sub-5ms INT8 quantized multi-metric landmark pipelines with NIR robustness on sub-$100 edge hardware.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 7: Objectives
Develop a 100% offline Non-IoT Edge driver monitoring system executing in under 5 ms frame latency (200+ FPS capability).
Implement mathematical models for Eye Aspect Ratio (EAR), Mouth Aspect Ratio (MAR), PERCLOS, and 3D Head Pose Euler angles.
Design a 4-stage compression pipeline (Architecture Selection -> Knowledge Distillation -> Structured Pruning -> QAT INT8).
Achieve 24/7 lighting robustness using active NIR (850nm/940nm) illumination and adaptive CLAHE contrast enhancement.
Provide eyewear robustness with an automated fallback scoring matrix for dark and mirrored sunglasses.
Deploy and benchmark on sub-$100 hardware (RPi 5 + Google Coral / Hailo-8L) and NVIDIA Jetson Orin Nano.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 8: Required Tools and Technology
Hardware Platforms: Raspberry Pi 5 ($35), Google Coral USB Edge TPU ($60), Hailo-8L 13 TOPS HAT ($70), NVIDIA Jetson Orin Nano ($249).
Optical Hardware: Near-Infrared (NIR) 850nm/940nm LED arrays, narrow bandpass optical filters, No-IR-Cut camera sensor.
Programming Runtimes: Python 3.10+ & C++17 for high-performance multithreaded frame ingestion and inference.
Vision & AI Runtimes: OpenCV 4.8+ (CLAHE, V4L2 pipeline), MediaPipe Tasks API (468 3D landmarks), TFLite INT8 (XNNPACK), TensorRT 8.6+, HailoRT.
ML Classifiers & HMI: Scikit-Learn (SVM RBF classifier for 4-level fatigue grading), RPi.GPIO / python-can for physical buzzer & CAN bus alert output.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 9: Method/ Approach
Stage 1 - Preprocessing: V4L2 NIR frame capture (1080p@30fps) -> Color space conversion -> Adaptive CLAHE (clipLimit=4.0, grid 8x8).
Stage 2 - Edge AI Inference: BlazeFace face detection (1.5ms) -> 468-point Face Mesh INT8 landmark extraction (2.5ms).
Stage 3 - Metric & Calibration: Compute EAR, MAR, PERCLOS, and 3D Head Pose via cv2.solvePnP(). Auto-calibrate baseline in < 10 seconds.
Stage 4 - Compression Pipeline: Teacher ResNet-50 distillation -> 30% structured channel pruning -> 5-epoch Quantization-Aware Training (QAT INT8).
Stage 5 - Classification & Alerting: 3-Feature SVM (PERCLOS + EAR + MAR) evaluates fatigue severity (Level 0: Alert -> Level 3: Micro-sleep Hazard) in < 0.1ms.
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY

## Slide 10: Bibliography
[R1] Soukupova, T., & Cech, J. (2016). Real-Time Eye Blink Detection Using Facial Landmarks. Computer Vision Winter Workshop.
[R2] Dinges, D. F., & Grace, R. (1998). PERCLOS: A Valid Psychophysiological Measure of Alertness. US Dept of Transportation.
[R3] Dzyakanchuk, A., et al. (2022). Low-Power Face Detection on Raspberry Pi for Automotive DMS. IEEE Access.
[R4] Acharjee, S., et al. (2020). Edge-Based Driver Drowsiness Monitoring on Embedded Hardware. SN Computer Science.
[R5] Garces, M., et al. (2021). Automated Yawn Detection Using Mouth Aspect Ratio. IEEE Sensors Journal.
[R6] MediaPipe Face Mesh Topology (468 3D Landmarks). Google AI Edge Documentation (2023).
[R7] NVIDIA TensorRT INT8 Developer Guide for Jetson Orin Platform (2024).
[R8] Hailo-8L Dataflow Compiler & Software Suite User Guide (2024).
DEPARTMENT OF COMPUTER ENGINEERING
*Proprietary material of SILVER OAK UNIVERSITY